## Slide 1: Appendicitis Point of Care Ultrasound

## Slide 2: Outline
Indications and relative contraindications
Appendix anatomy including anatomical variants
Patient positioning and scanning technique
Clinical integration

## Slide 3: The right patient for RLQ POCUS
Clinical concern for appendicitis (RLQ pain, fever, anorexia, nausea, vomiting)
Pain is thoughtfully managed
Immediate surgery is not a better option
You are not evaluating a large differential diagnosis (often the case in elderly pts)
Trying to avoid radiation exposure (young, pregnant, other)
No access to other imaging (CT/MRI)

## Slide 4: The right patient for RLQ POCUS
Clinical concern for appendicitis (RLQ pain, fever, anorexia, nausea, vomiting)
Pain is thoughtfully managed
Immediate surgery is not a better option
You are not evaluating a large differential diagnosis (often the case in elderly pts)
Trying to avoid radiation exposure (young, pregnant, other)
No access to other imaging (CT/MRI)

## Slide 5: The right patient for RLQ POCUS
Clinical concern for appendicitis (RLQ pain, fever, anorexia, nausea, vomiting)
Pain is thoughtfully managed
Immediate surgery is not a better option
You are not evaluating a large differential diagnosis (often the case in elderly pts)
Trying to avoid radiation exposure (young, pregnant, other)
No access to other imaging (CT/MRI)
Pediatrics
Young adults
Pregnant patients
Many others! Consider each case.
=

## Slide 6: Appendix Anatomy
The appendix is located in the RLQ originating from the cecum
Commonly found overlying the iliac artery/vein
Cecum
Appendix
Iliac A.

## Slide 7: Appendix Anatomy
The appendix is located in the RLQ originating from the cecum
Commonly found overlying the iliac artery/vein AND psoas muscle

## Slide 8: Appendix Anatomy Variants…
The appendix is actually only above the iliacs about 1/3 of the time
More likely, it is found behind the cecum, where there less well defined landmarks

## Slide 9: Probe Selection
Linear is good for image resolution
Curvilinear is good for tissue penetration

## Slide 10: Patient Positioning
Scanning is done in the supine position
If tolerable, crossing the patient’s right leg over the left may help bring appendix more anterior

## Slide 11: Scanning technique: point of most pain
Have the patient point to the location of most intense pain and put the probe there
Transverse view -> indicator to patient’s right
Sagittal -> indicator to patient’s head

## Slide 12: Scanning technique: systematic
Search systematically for the appendix or landmarks
Appendix should be bounded by:
  Iliac crest (lateral)
  Iliac a/v (medial)
  Psoas (posterior)
Keep the indicator up or to the right

## Slide 13: Ultrasound findings in normal appendix
Tubular structure (<6 mm diameter)
Compressible
Non-peristaltic
Proximal portion originates from the cecum

## Slide 14: Ultrasound findings in normal appendix

## Slide 15: Ultrasound findings in normal appendix
VS Small bowel
Peristalsing with luminal contents
VS Large bowel (cecum)
Large stx with “dirty air pattern”

## Slide 16: Ultrasound signs of acute appendicitis
Primary Criteria
Non-compressibility
Diameter >6 mm

## Slide 17: Ultrasound signs of acute appendicitis
Primary Criteria
Non-compressibility
Diameter >6 mm

## Slide 18: Ultrasound signs of acute appendicitis
Primary Criteria
Non-compressibility
Diameter >6 mm

## Slide 19: Ultrasound signs of acute appendicitis
Primary Criteria
Non-compressibility
Diameter >6 mm

## Slide 20: Ultrasound signs of acute appendicitis
Primary Criteria
Non-compressibility
Diameter >6 mm
Secondary Signs
Appendicolith – hyperechoic with posterior shadowing
Free fluid surrounding appendix
Mural hyperemia on color Doppler
Hyperechoic local mesenteric fat
Target sign
  Hypoechoic fluid
  Hyperechoic mucosa/submucosa
  Hypoechoic muscularis

## Slide 21: Acute appendicitis

## Slide 22: Acute perforated appendicitis
Findings:
Free fluid surrounding non-compressible tubular structure which overlies the iliac artery and psoas muscle
Mural hyperemia on Doppler

## Slide 23: Acute Appendicitis
Findings: dilated blind ended tubular structure overlying iliac vessels and originating from the cecum with large fecolith

## Slide 24: Acute Appendicitis
Iliac vessels
Psoas muscle

## Slide 25: A-line pattern (abdomen)

## Slide 26: A-line pattern (abdomen)
Prominent A-line pattern in abdomen suggests intraabdominal free air

## Slide 27
Findings: dilated blind ended tubular structure overlying iliac vessels with surrounding hyperechogenic fat
Acute Appendicitis

## Slide 28: Interpreting Findings (when to CT)
Appendix Fully Visualized
High suspicion
Suspected
Low suspicion
Equivocal Findings
Appendix was not fully visualized and there are some secondary signs of appendicitis
Appendix NOT visualized
- Ongoing area of research
Likely does not need CT
Probably needs a CT
If few S/S: no CT
If many S/S: CT

## Slide 29: Summary
Consider ultrasound as a first line diagnostic tool in select patients
Scan over point of most tenderness or systematically
Look for a blind ending, non-peristalsing, tubular structure
Non-compressibility and >6 mm width are diagnostic for appendicitis
Integrate test findings with overall clinical scenario

## Slide 30
Findings: dilated tubular structure with hyperemia on Doppler
Target sign
Ring of fire sign
Acute Appendicitis

## Slide 31: Acute Appendicitis
Findings: tip of appendix