## Slide 1: Appendicitis Point of Care Ultrasound

## Slide 2: Outline
Indications and relative contraindications
Appendix anatomy including anatomical variants
Patient positioning and scanning technique
Clinical integration

## Slide 3: The right patient for RLQ POCUS
Clinical concern for appendicitis (RLQ pain, fever, anorexia, nausea, vomiting)
Pain is thoughtfully managed
Immediate surgery is not a better option
You are not evaluating a large differential diagnosis (often the case in elderly pts)

## Slide 4: Appendix Anatomy
The appendix is located in the RLQ originating from the cecum
Commonly found overlying the iliac artery/vein

## Slide 5: Appendix Anatomy
The appendix is located in the RLQ originating from the cecum
Commonly found overlying the iliac artery/vein AND psoas muscle

## Slide 6: Appendix Anatomy Variants…
The appendix is actually only above the iliacs about 1/3 of the time
More likely, it is found behind the cecum, where there less well defined landmarks

## Slide 7: Probe Selection
Linear is good for image quality
Curvilinear is good for tissue penetration

## Slide 8: Patient Positioning
Scanning is done in the supine position
If tolerable, crossing the patient’s right leg over the left may help bring appendix more anterior

## Slide 9: Scanning technique: point of most pain
Have the patient point to the location of most intense pain and put the probe there
Transverse view -> indicator to patient’s right
Sagittal -> indicator to patient’s head

## Slide 10: Scanning technique: systematic
Search systematically for the appendix or landmarks
Appendix should be bounded by:
  Iliac crest (lateral)
  Iliac a/v (medial)
  Psoas (posterior)
Keep the indicator up or to the right

## Slide 11: Ultrasound findings in normal appendix
Tubular structure (<6 mm diameter)
Compressible
Non-peristaltic
Proximal portion originates from the cecum

## Slide 12: Ultrasound findings in normal appendix
VS Small bowel
Peristalsing with luminal contents
VS Large bowel (cecum)
Large stx with “dirty air pattern”

## Slide 13: Ultrasound signs of acute appendicitis
Primary Criteria
Non-compressibility
Diameter >6 mm
Secondary Signs
Appendicolith – hyperechoic with posterior shadowing
Free fluid surrounding appendix
Mural hyperemia on color Doppler
Hyperechoic local mesenteric fat
Target sign
  Hypoechoic fluid
  Hyperechoic mucosa/submucosa
  Hypoechoic muscularis

## Slide 14: Acute perforated appendicitis
Findings:
Free fluid surrounding non-compressible tubular structure which overlies the iliac artery and psoas muscle
Mural hyperemia on Doppler

## Slide 15: Acute Appendicitis
Findings: dilated non-compressible tubular structure overlying the iliac artery

## Slide 16
Findings: incompletely viewed dilated blind ending tubular structure with “target sign” and appendicolith
Acute Appendicitis

## Slide 17
Findings: dilated non-compressible tubular structure demonstrating target sign and fecolith
Acute Appendicitis

## Slide 18: Acute Appendicitis
Findings: dilated blind ended tubular structure overlying iliac vessels and originating from the cecum with large fecolith

## Slide 19: Acute Appendicitis
Findings: tip of appendix

## Slide 20: A-line pattern (abdomen)
Prominent A-line pattern in abdomen suggests intraabdominal free air

## Slide 21
Findings: dilated blind ended tubular structure overlying iliac vessels with surrounding hyperechogenic fat
Acute Appendicitis

## Slide 22
Findings: dilated tubular structure with hyperemia on Doppler
Target sign
Ring of fire sign
Acute Appendicitis

## Slide 23: Interpreting Findings (when to CT)
Appendix Fully Visualized
High suspicion
Suspected
Low suspicion
Equivocal Findings
Appendix was not fully visualized and there are some secondary signs of appendicitis
Appendix NOT visualized
- Ongoing area of research
Likely does not need CT
Probably needs a CT
If few S/S: no CT
If many S/S: CT

## Slide 24: Summary
Consider ultrasound as a first line diagnostic tool in select patients
Scan over point of most tenderness or systematically
Look for a blind ending, non-peristalsing, tubular structure
Non-compressibility and >6 mm width are diagnostic for appendicitis
Integrate test findings with overall clinical scenario